## Slide 1: Competitive Intelligence Report

## Slide 2: Overview
This report is a consolidation of the findings from researching the following topics over the past couple weeks:
  Blood Sugar Prediction Tablestakes
  Competitors & Competitive Advantage
  Data Processing & ML Model Development
The objective of the research was to obtain a deeper understanding of 1) the requirements to obtain FDA approval, 2) what our competitors are doing & how we are differentiated, and 3) what processes should we develop to process data and obtain an accurate glucose prediction
See the following documents for my detailed notes:
  Research Paper Folder
  Gluco Data Processing + Personalization Modeling
  Background + Competitive Research
  General Notes & Thoughts Regarding Non-Invasive Glucose Challenges

## Slide 3: Challenges & Solutions to Non-Invasive Glucose Monitoring
There are a multitude of challenges faced with bringing a non-invasive glucose monitoring solution to market, the main one’s being:
  Data Availability & Reliability
    Machine learning approaches require the availability of enough data for training to generalize well for unseen data
  Model Selection & Reliability
    Considerations include using an ensemble of different models, interpretability or explainability of the chosen model, ensuring the size of the model fits on the wearable device, personalization, and more
  Security & Privacy
  Utility & User Acceptance
For a successful launch, Gluco has to address all of these better than any other competitor

## Slide 4: Challenges & Solutions to Non-Invasive Glucose Monitoring (cont.)
Unsurprisingly, we are mostly aware of the different methods researchers, startups, and organizations have tried to make this a reality (and overcome these challenges):
  Optical Methods
    Near-Infrared (NIR) Spectroscopy
    Raman Spectroscopy
    Fluorescence Spectroscopy
    Optical Coherence Tomography (OCT)
  Electromagnetic Methods
    Radiofrequency (RF) Technology
    Microwave Sensing
  Ultrasound and Acoustic Methods
  Electrochemical Methods
  Thermal Methods
  Bio-impedance Spectroscopy
  Photonic and Fiber Optic Sensors
  Fluorescence-Based Methods
  Magnetic Resonance
  Reverse Iontophoresis
  Polarimetry

## Slide 5: Challenges & Solutions to Non-Invasive Glucose Monitoring (cont.)
Despite all of these different methods, the optical methods seem the most promising
In addition to the promising nature of the accuracy, optical methods also benefit from being widely used and studied, this will make the technology that underpins Gluco integratable into other systems
However, given this seemingly obvious fact, the solution is going to lie more so within the data processing and machine learning model than the higher level methodology

## Slide 6: Accuracy Requirements
The mean absolute relative difference (MARD) and the Clarke error grid analysis (CEGA) plot are used to assess the accuracy of blood glucose measuring devices
  The MARD is an average value of all absolute percentage errors
The CEGA plot is one that is divided into 5 zones: A, B, C, D, and E
  Zone A has error values <20% with respect to the reference
  Zones B, C, D, and E can have different and higher error ranges
According to the FDA, for adjunctive use, a blood glucose measurement device must have a MARD of 20 mg/dL for sensor glucose values <100 mg/dL and 20% for sensor glucose values "100 mg/dL for adjunctive use[9,10]
  The criteria becomes tighter for non-adjunctive cases (when devices make insulin dosing decisions without confirming with a fingerstick); the blood glucose measurement device must have a MARD of 10 mg/dL for sensor glucose values <100 mg/dL and 10% for sensor glucose values "100 mg/dL

## Slide 7: Accuracy Requirements (cont.)
There are only a few FDA approved CGMs on the market, all of which are invasive in nature:
  G6 (9% MARD) from Dexcom
  FreeStyle Libre 2 (9.3% MARD) and Libre 3 (9.7% MARD) from Abbott
  Guardian Sensor 3 (9.4% MARD) and Guardian Connect (10.2% MARD) from Medtronic
  Eversense (9.6% MARD) from Senseonic
When it comes to non-invasive sensors, there are some that do reach high accuracy:
  Integrity Applications’ GlucoTrack (23.4% MARD, 57% in zone A)
  CNOGA’s CoG (17.1% MARD, 86.2% in zone A)
Although there have been many developments in the field of noninvasive sensing technology, no device has yet received FDA approval

## Slide 8: Accuracy Requirements (cont.)
Regulation | Glucose Level | Acceptable Error Range | Device Accuracy | MARD
US FDA | Entire Range | -15% ~ 15% | > 95% | < 5%
 |  | -20% ~ 20% | > 99% | < 1%
European Medicines Health Canada CFDA | >/= 100mg/dL | -15% ~ 15% | > 95% | < 5%
 | < 100mg/dL | -15 ~ 15 mg/dL | > 95% | < 5%

## Slide 9: Accuracy Requirements (cont.)
Product Name | Manufacturer | Sensing Technology | Accuracy
GlucoTrack | Integrity Application | Multi-technology (Ultrasound + Thermal + Electromagnetic) | MARD: 23.4% Zone A: 57% Zone B: 39%
Combo Glucometer (CoG) | CNOGA Medical | Near-Infrared Spectroscopy | MARD: 17.1% Zone A: 86.2% Zone B: 12.6%
SugerBEAT | Nemaura Medical | Reverse Iontophoresis | MARD: 13.8%
Symphony | Echo Therapeutics | Sonophoresis | MARD: 12.3% Zone A: 81.7% Zone B: 18.3%
Wizmi | Wear2b Ltd | NIR spectroscopy | MARD: 7.2% Zone A: 93% Zone B: 7%
Eversense | Senseonics | Fluorescence | MARD: 14.8%

## Slide 10: Accuracy Requirements (cont.)
Combo Glucometer (CoG) by Cnoga Medical is one of the best performing non-invasive blood glucose monitors commercially available
  It uses near-infrared spectroscopy technology
  It consists of four LEDs and four sensors to analyze absorption and scattering patterns
  The sensor data is analyzed using a neural network algorithm
Even though it is one of the best performing devices, it has a MARD of 17.1% which is still much higher than the FDA requirement.
SugerBEAT, Symphony, Wizmi, and Eversense are minimally invasive

## Slide 11: Competitive Advantage
Hardware
  The NSP32m seems like it could be a differentiating piece of hardware, along with the data produced from it
Data Processing & Machine Learning Model
  We need to develop a process and model that is differentiated from what has been tested. This will be a combination of robust artifact removal and a personalized model
Robust Dataset
  In addition to PPG signals, absorption spectrum data, IMU data, and the like, we will have data collected in real-world scenarios with a variety of different body types and physiological states (from the pre-order). This will give us a major data advantage.
Market Knowledge
  We need to ensure we learn about the customer through qualitative interviews, so that we can know them better than any competitor
Brand
  Vibes

## Slide 12: Data Processing & ML Model Development
Gluco Data Processing Flow:
Data Collection
  Gluco sends data to Gluco App
Gluco App Sends Raw Data to Cloud
Data Processing
  Within the Gluco App, the data goes through the following process: Signal Preprocessing (filtering, normalization/standardization) → Noise and Artifact Reduction (motion artifacts) → Signal Smoothing
Gluco App Sends Processed Data to Cloud
Feature Extraction
  Within the Gluco App, the processed data is used to extract the following features: [INSERT FEATURES TO EXTRACT]
Gluco App Sends Extracted Features to Cloud
Gluco App Predicts Blood Sugar from Extracted Features
Gluco App Sends Blood Sugar Estimates to Cloud (Along with Relevant Features)

## Slide 13: Data Processing & ML Model Development (cont.)
Generalized Fine-Tuning Approach for Personalization:
Overview:
The goal is to develop a robust machine learning model (Model A) using a general set of features (X) and then personalize it for specific users by incorporating additional features (X + additional features) to create Model B. This approach ensures that Model B is tailored to individual users while leveraging the broad knowledge captured by Model A.

## Slide 14: Data Processing & ML Model Development (cont.)
Generalized Fine-Tuning Approach for Personalization:
Step-by-Step Process:
Data Preparation
Training Model A
Expanding for Personalization
Fine-Tuning Model B
Validation and Testing
See this document for more detail

## Slide 15: Data Processing & ML Model Development (cont.)
High-Level Development Roadmap:
Data Collection and Management
Synthetic Data Generation
Data Exploration and Understanding
Data Pre-processing
Feature Engineering
Model Selection and Development
Model Training and Validation
Model Optimization and Testing
Applications to Real Data